## Slide 1
GE100 - Application of Information and Communication Technologies
Instructor: Alina Maryum
Lec # 4: System Unit-Processing and Memory

## Slide 2: Learning Objectives
Understand how data and programs are represented to a computer and be able to identify a few of the coding systems used to accomplish this
Explain the functions of the hardware components commonly found inside the system unit, such as the CPU, GPU, memory, buses, and expansion cards
Describe how peripheral devices or other hardware can be added to a computer
Understand how a computer’s CPU and memory components process program instructions and data
Name and evaluate several strategies that can be used today to speed up the operations of a computer
List some processing technologies that may be used in future computers

## Slide 3: Data and Program Representation
Digital Data Representation
  Coding Systems
    Used to represent data and programs in a manner understood by computer
  Digital Computers
    Can only understand two states, off and on (0 and 1)
  Digital Data Representation
    The process of representing data in digital form so it can be understood by a computer

## Slide 4
    Bit
      The smallest unit of data that a computer can recognize
    Byte = 8 bits
      Eight bits grouped together are collectively referred to as a byte
      Document size, storage capacity, and memory capacity are all measured in bytes
    Prefixes are often used to express larger quantities of bytes: kilobyte (KB), megabyte (MB), gigabyte (GB), terabyte (TB), petabyte (PB), exabyte (EB), zettabyte (ZB), yottabyte (YB)
Data and Program Representation

## Slide 5: Representing Numerical Data
Numbering System
  A way of representing numbers
  Decimal numbering system
    Uses 10 symbols (0-9)
  Binary numbering system
    Uses only two symbols (1 and 0) to represent all possible numbers
  In both systems, the position of the digits determines power or exponent to which base number is raised
    10 for decimal
    2 for binary

## Slide 6: Representing Numerical Data

## Slide 7: Coding Systems for Text-Based Data
Text-based data is represented by binary coding systems specifically developed for text-based data
  ASCII
  EBCDIC
  Unicode
These codes represent all characters that can appear in text data
  Numbers
  Letters
  Special characters and symbols like the dollar sign, comma, percent symbol, and mathematical symbols

## Slide 8: Coding Systems for Text-Based Data
ASCII (American Standard Code for Information Interchange)
  Coding system traditionally used with personal computers
  7-digit (7-bit) code
  Several different 8-bit extended versions of ASCII
EBCDIC (Extended Binary-Coded Decimal Interchange Code)
  Developed by IBM, primarily for mainframes
  Unique combination of 8 bits (1 byte), which allows 256 (28) unique combinations

## Slide 9: Coding Systems for Text-Based Data
Unicode
  Universal coding standard designed to represent text-based data
  written in any ancient or modern language
  Longer code, consisting of 8 to 32 bits per character, and can represent over one million characters
  Replacing ASCII as the primary text-coding system
  Includes ASCII character set so ASCII data can be converted easily to Unicode when needed
            Used by most Web browsers, pages, and applications
            Latest versions of Microsoft Windows, Office, OS X
            Modern programming languages, such as Java and Python
            Updated regularly to add new characters

## Slide 10: Coding Systems for Other Types of Data
Graphics Data (still images such as photos or drawings)
  Bitmapped images
    Image made of up of a grid of small dots called pixels
    Monochrome graphic can only be one of two colors
      Requires just one bit for color storage
    Images with more than two colors
      Can use 4, 8, or 24 bits to store the color data for each pixel
  More bits = more colors

## Slide 11: Coding Systems for Other Types of Data

## Slide 12: Coding Systems for Other Types of Data
Audio Data
  Must be in digital form in order to be stored on or processed by computer
  Often compressed when sent over the Internet
    MP3 files are 10 times smaller than their uncompressed digital versions
    Download more quickly and take up less storage space
Video Data
  Displayed using a collection of frames, each frame contains a still image
  Amount of data can be substantial but can be compressed

## Slide 13: Representing Software Programs
Machine language
  Binary-based programming language, consisting only of 0s and 1s, that a computer can execute directly
  Early programs were written in machine language
  Today’s programs still need to be translated into machine language in order to be understood by the computer

## Slide 14: Inside the System Unit
System Unit
  The main case of a computer or mobile device
  Houses the processing hardware for a computer as well as other components, such as storage devices, the power supply, and cooling hardware
  With a desktop computer, usually looks like a rectangular box
  Contains one or more processors, several types of memory, interfaces to connect external peripheral devices (such as printers), and other components all interconnected through sets of wires called buses on the motherboard

## Slide 15: Inside the System Unit

## Slide 16: Inside the System Unit
1. Motherboard
      Main circuit board of a computing device
      Located inside the system unit, to which all computer system components connect
      – Computer Chip (called integrated circuits (ICs))
      • Contain interconnected components (such as transistors) that enable electrical current to perform particular functions
      – Circuit Board
    Thin board containing computer chips and other electronic components

## Slide 17: Inside the System Unit
Motherboard has a variety of chips, boards, and connectors attached to it
All devices used with a computer need to be connected via a wired or wireless connection to motherboard
External devices (monitors, keyboards, mice, printers) plugging into a port— special connector exposed through the exterior of the system unit case
Wireless devices use either a transceiver that plugs into a port on the computer to transmit data between the wireless device and the motherboard or wireless networking technology such as Bluetooth, Wi-Fi

## Slide 18: Inside the System Unit
2. Power Supply and Drive Bays
  Power Supply
  Most personal computers plug into a standard electrical outlet
  Power supply inside a computer delivers electricity to the computer via a power cord
  Portable computers and mobile devices contain rechargeable battery packs, which are charged via a power outlet
  Drive Bay
  Rectangular metal racks inside system unit into which storage devices can be inserted
    Hard drive, DVD drive, flash memory card reader
    Connected to the motherboard with a cable

## Slide 19: Inside the System Unit
3. Processors
                A chip (such as the CPU or GPU) that performs processing functions
                Circuitry and components packaged together and connected directly to the motherboard
  The CPU (Central Processing Unit)
    The chip located on motherboard of a computer
    Performs most of the processing for a computer
    Also called Microprocessor for personal computer
    Typically designed for a specific type of computer, such as for desktop computers, servers, portable computers (like notebook and tablet computers), or mobile devices (like tablets and smartphones)

## Slide 20: Inside the System Unit
Typically different CPUs for desktop computers, portable computers, servers, mobile devices, consumer devices, etc.
  Personal computer CPU often made by Intel or AMD
  Media tablets and mobile phones use processors made by other companies such as ARM

## Slide 21: Inside the System Unit
Dual-core CPU
  Contains two separate processing cores
Quad-core CPU
  Contains four separate processing cores
Multi-core CPU
  Contain the processing components or cores of multiple independent processors on a single CPU
  Allow computers to work on more than one task at a time
  Typically experience fewer heat problems than single-core CPU
  Each core typically runs slower than a single-core CPU, although total processing power of the multi-core CPU is greater
  Increase performance of mobile devices while, at the same time, delivering better battery life

## Slide 22: Inside the System Unit
Most support virtualization and other recent technologies
CPUs used in desktop computers typically have 4 cores
Server processors may have 15 cores or more
Mobile processors
        Typically run a little slower than comparable desktop CPUs
        But they are often multi-core and they run cooler
        Consume less power to allow devices to run longer on battery power without a recharge

## Slide 23: Inside the System Unit

## Slide 24: Inside the System Unit
4. GPU (Graphics Processing Unit)
  Takes care of the processing needed to display images (including still images, and animations) on the screen
  Can be located on motherboard, on video graphics board, or both CPU and GPU integrated into CPU package

## Slide 25: Inside the System Unit
Processing Speed
  CPU clock speed is one measurement of processing speed
  Rated in megahertz (MHz) or gigahertz (GHz)
  Higher CPU clock speed = more instructions processed per second
  Alternate measure of processing speed is the number of instructions a CPU can process per second
    Megaflops (millions), gigaflops (billions), teraflops (trillions)
  Benchmark tests can be used to evaluate overall processing speed

## Slide 26: Inside the System Unit
Word Size
  The amount of data that a CPU can manipulate at one time
  Typically 32-bit or 64-bit
  Usually, a larger word size allows for faster processing and use of more RAM
Cache Memory
  Special group of very fast memory chips located on or close to the CPU
  Level 1 is fastest, then Level 2, then Level 3
  More cache memory typically means faster processing
  Usually internal cache (built into the CPU)

## Slide 27: Inside the System Unit
Bus Width, Bus Speed, and Bandwidth
  Bus is an electronic path over which data can travel
  Found inside the CPU and on the motherboard
  Bus width is the number of wires in the bus over which data can travel
    A wider bus allows more data to be transferred at one time
  Bus speed determines the bus’s bandwidth—that is, the amount of data that can be transferred via the bus in a given time period
  Amount of data actually transferred under real-life conditions is called throughput

## Slide 28: Inside the System Unit
5. Memory
  Refers to chip-based storage located inside the system unit
  Storage refers to the amount of long-term storage available to a computer
  Random Access Memory (RAM)
    Computer’s main memory
    Consists of chips arranged on a circuit board called a memory module which are plugged into motherboard
    Stores essential parts of operating system, programs, and data computer is currently using

## Slide 29: Inside the System Unit
Volatile
  RAM content lost when the computer is shut off
  ROM and flash memory are non-volatile
Measured in bytes
  Amount installed depends on the CPU and operating system being used
Like the CPU, RAM consists of electronic circuits etched onto chips
Smartphones and other mobile devices typically use embedded memory chips
Memory chips for servers and personal computers are typically arranged onto circuit boards called memory modules, which, in turn, are plugged into motherboard

## Slide 30: Inside the System Unit
Most desktop and server memory modules are dual in-line memory modules DIMMs
Notebook computers are smaller small outline DIMMs or SO-DIMMs
Smaller devices even smaller are Mini-DIMMs or Micro-DIMMs
Most personal computers today use SDRAM (synchronous dynamic RAM)
SDRAM is available in several DDR (double-data rate) versions, including DDR2, DDR3, and DDR4.
To further improve memory performance, memory typically uses a dual-channel memory architecture, which has two paths that go to and from memory and so it can transfer twice as much data at one time as single-channel memory architecture of the same speed.
Notes: It is called "dynamic" because it requires constant refreshing to maintain the data stored in its memory cells,
his synchronization improves its speed and performance by allowing it to send and receive data in sync with the CPU, reducing the time the processor spends waiting for memory operations.

## Slide 31: Inside the System Unit
Each location in memory has an address
  Each location typically holds one byte
  Whenever a block of data, instruction, program, or result of a calculation is stored in memory, it is usually stored in one or more consecutive addresses, depending on its size
  Computer system sets up and maintains directory tables to facilitate retrieval of the data

## Slide 32: Inside the System Unit
Registers
  High-speed memory built into the CPU
  Used to store data and intermediary results during processing
  Fastest type of memory even faster than Level 1 cache
ROM (read-only memory)
  Non-volatile chips located on the motherboard into which data or programs have been permanently stored
  Retrieved by the computer when needed
  Neither write over the data or programs in ROM chips
  Used to store the permanent instructions referred to as firmware
  Being replaced with flash memory

## Slide 33: Inside the System Unit
Flash Memory
  Nonvolatile memory chips that can be used for storage
  Have begun to replace ROM for storing system information
  Now stores firmware for personal computers and other devices
  Built into many types of devices (media tablets, mobile phones, and digital cameras) for user storage

## Slide 34: Inside the System Unit
6. Fans and Heat Sinks
  Heat is an ongoing problem for CPU and computer manufacturers
    Can damage components
    Cooler chips run faster
  Use fans and heat sinks (small components typically made out of aluminum with fins) that help to dissipate heat
  Liquid cooling systems cool the computer with liquid-filled tubes
  Immersion cooling hardware is actually submerged into units filled with liquid cooling solution
  Notebook cooling stand cools the underside of a notebook computer
  Other cooling methods, such as ion pump cooling systems, are under development

## Slide 35: Fans, heat sinks, and Other Cooling Components

## Slide 36: Inside the System Unit
  7. Expansion Slot and Expansion Cards
  Expansion Slot
    A location on the motherboard into which expansion cards are inserted
  Expansion Card
    A circuit board inserted into an expansion slot
    Used to add additional functionality or to attach a peripheral device
Notes: GPU, NIC, Sound Card etc.

## Slide 37: Inside the System Unit
8. Bus
Electronic path within a computer over which data travel. It is Located within the CPU and etched onto the motherboard
  Expansion Bus- Connects the CPU to peripheral (typically input and output) devices
  Memory Bus- Connects CPU directly to RAM
  Frontside Bus (FSB)
    Connects CPU to the chipset that connects the CPU to the rest of the bus architecture
    Use special highspeed technologies. Intel uses its QuickPath Interconnect (QPI) technology and AMD uses its HyperTransport Technology

## Slide 38: Inside the System Unit
PCI (Peripheral Component Interconnect) and PCI Express (PCIe) Bus
  PCI has been one of the most common types
  PCI Express (PCIe) bus (which connects to the PCI bus) is more often used for expansion
  Available in several different widths
  16-bit version of PCIe (referred to as PCIe x16) is commonly used with video graphics cards to connect a monitor to a desktop computer
  Expansion cards for other peripherals often connect via the 1-bit PCIe bus (referred to as PCIe x1)
  Extremely fast—the current version (PCIe 4.0) transfers data at 16 Gbps (billions of bits per second) per lane

## Slide 39: Buses

## Slide 40: Inside the System Unit
Universal Serial Bus (USB)
  Extremely versatile
  Allows 127 different devices to connect to a computer via a single USB port
  Original USB standards are relatively slow
    USB 1.0 transfer data at 12 Mbps
    USB 2.0 transfer data at 480 Mbps
  Newest standards (also called SuperSpeed USB) are much faster
    USB 3.0 transfer data at 5 Gbps
    USB 3.1 transfer data at 10 Gbps
    USB 3 also supports faster and more powerful charging
    Identify USB 3 ports, they are coloured blue

## Slide 41: Inside the System Unit
9. Port and Connectors
  Connectors located on the exterior of a computer’s system unit that are used to connect external hardware devices
  Each port is attached to the appropriate bus on the motherboard so that when device is plugged into a port, the device can communicate with CPU and other computer components
  Ports often found on a desktop or notebook computer
    USB, Audio, and HDMI, Network, Flash memory card slot, DisplayPort
  Mobile devices often use smaller versions, such as micro-USB and micro-HDMI

## Slide 42: Ports and Connectors
Typical Ports

## Slide 43: Ports and Connectors
Typical Connectors

## Slide 44: Inside the System Unit
Various types of ports
  Monitor ports
    Used to connect a monitor to a computer via an HDMI (High-Definition Multimedia Interface)
    Additional monitor to a tablet or other mobile device, a Mini-HDMI port or even smaller Micro-HDMI
  Network ports
    Used to connect a computer to a computer network via a networking cable—typically a cable using an RJ-45 connector
  USB ports
    Used to connect USB devices (such as keyboards, mice, printers, hard drives, and digital cameras)

## Slide 45: Inside the System Unit
  IrDA (Infrared Data Association) and Bluetooth ports
    Used to receive wireless transmissions from devices
    IrDA ports are commonly used to “beam” data from a portable computer or mobile device to a computer
    Bluetooth ports are most often used with wireless keyboards, mice, speakers, and headsets
  Flash memory card slots
    Used to connect flash memory cards or other hardware using a flash memory card interface

## Slide 46: Inside the System Unit
  Audio ports
    Used to connect speakers, headphones, or a microphone to the computer
  eSATA (external SATA) ports
    Used to connect external SATA devices (external hard drive)
    External hard drives that connect via eSATA are much faster than external hard drives that connect via a USB
  Thunderbolt ports
    Available primarily on some Apple devices
    Used to connect peripheral devices (such as storage devices and monitors) via Thunderbolt cables
    Latest version of Thunderbolt, Thunderbolt 3, is extremely fast, 40 Gbps
Notes: Serial Advanced Technology Attachment

## Slide 47: Inside the System Unit
Most computers today support the Plug and Play standard
  Computer automatically configures new devices as soon as they are installed and the computer is powered up
Tablets have ports similar to desktop and notebook computers, but they often have fewer of them
Smartphones tend to have a more limited amount of expandability
  Have a USB port
  Flash memory card slot
  Subscriber Identify Module (SIM) slot to hold a SIM card used to connect that device to a mobile phone network

## Slide 48: Inside the System Unit
USB hubs
This USB hub is used to connect multiple USB-A and USB-C devices to a
single USB-C port

## Slide 49: Inside the System Unit
Typical ports for tablets and tablet docks

## Slide 50: How the CPU Works
CPU (Central Processing Unit)
  Consists of a variety of circuitry and components packaged together
  Transistor: Key element of the microprocessor
    Made of semi-conductor material that acts like a switch controlling the flow of electrons inside a chip
  Today’s CPUs contain hundreds of millions of transistors
  Moore’s Law Number doubles about every 18 months
    In 1965, Gordon Moore predicted that the number of transistors per square inch on chips had doubled every two years and that trend would continue
    Moore’s Law is still relevant today for processors as well as other computer components

## Slide 51: How the CPU Works
Typical CPU Components
  Arithmetic/Logic Unit (ALU)
    Performs arithmetic involving integers and logical operations
  Floating Point Unit (FPU)
    Performs decimal arithmetic
  Control Unit (CU)
    Coordinates and controls activities within a CPU core
  Prefetch Unit (PU)
    Attempts to retrieve data and instructions before they are needed for processing in order to avoid delays

## Slide 52: How the CPU Works
Decode Unit
  Translates instructions from the prefetch unit so they are understood by the control unit, ALU, and FPU
Registers and Internal Cache Memory
  Store data and instructions needed by the CPU
Bus Interface Unit
  Allows the core to communicate with other CPU components

## Slide 53: How the CPU Works

## Slide 54: The System Clock and the Machine Cycle
System Clock
  Small quartz crystal on the motherboard
  Timing mechanism within the computer system that synchronizes computer’s operations
    Sends out a signal on a regular basis to all computer components
    Each signal is a cycle
    Number of cycles per second is measured in hertz (Hz)
    One megahertz = one million ticks of the system clock

## Slide 55: The System Clock and the Machine Cycle
Many PC system clocks run at 200 MHz
CPU that is synchronized with system clock runs at either system clock speed or at a multiple of or a fraction of system clock speed
CPU clock speed of 2 GHz, uses a multiplier of 10, means CPU clock “ticks” 10 times during each system clock tick
During each CPU clock tick, one or more pieces of microcode are processed
CPU with a higher clock speed processes more instructions per second than same CPU with a lower CPU clock speed

## Slide 56: The System Clock and the Machine Cycle
Machine Cycle
– The series of operations involved in the execution of a single machine-level instruction
– Each machine cycle consists of four general operations
  Fetch
  Decode
  Execute
  Store

## Slide 57: Making Computers Faster and Better Now and in the Future
Improving the Performance of Your System Today
  Add more memory
  Perform system maintenance
    Uninstall programs properly
    Remove unnecessary programs from the Startup list
    Consider placing large files not needed on a regular basis on external storage
    Delete temporary files

## Slide 58: Making Computers Faster and Better Now and in the Future
Error check and defrag the hard drive periodically
Scan for viruses and spyware continually
Clean out dust once or twice a year
Buy a larger or second hard drive
Upgrade your Internet connection
Upgrade your video graphics card

## Slide 59: Making Computers Faster and Better Now and in the Future
  Pipelining
    Capability of a CPU or CPU core to begin processing a new instruction as soon as the previous instruction completes the first stage of the machine cycle
    Allows multiple instructions to be processed at one time
Strategies for Making Faster and Better Computers

## Slide 60: Making Computers Faster and Better Now and in the Future
  Multiprocessing and Parallel Processing
    Multiprocessing - Capability of a single computer to use multiple processors or multiple processing cores, usually to process multiple jobs at one time and to process those jobs faster than could be performed with a single processor
    Parallel processing - Processing technique that uses multiple processors or multiple processing cores simultaneously, usually to process a single job as fast as possible
    Use multiple processors to speed up processing

## Slide 61: Making Computers Faster and Better Now and in the Future
  Improved Architecture
    Smaller components, faster bus speeds, multiple CPU cores, support for virtualization, creating CPUs with an increasing number of cores and integrated GPUs
  Improved Materials
    Flexible electronic components
– Copper, high-k, graphene chip

## Slide 62: 3D Chips
Three-dimensional (3D) chips are a technique for packing an increasing number of components onto small chips
Components are layered, which cuts down on surface area required
Especially important with notebook computers and mobile devices that have limited room inside the system unit

## Slide 63: Summary
Data and Program Representation
Inside the System Unit
How the CPU Works
Making Computers Faster and Better Now and in the Future